## Slide 1: Sigma Delta Modulator – Original Topology
+
-
Analog Input
D
Q
R
C
LVDS Receiver
Reference Voltage
clk
Board
PLD
Integrator
DAC
1-bit ADC
Digital
Output
Notes: - This is the block diagram associated

## Slide 2
Original Topology - Comments
Advantages
  Minimal use of external components
  R,C tolerance not important
Disadvantages
  Poor DC performance
  On a 3.3V solution, good linearity only between 0V and 1V
Comments
  Solution not yet characterised over process/temperature
  Differences in gain and offset (not only between 2 different devices, but also between 2 channels within the same device) – which means the output of the ADC is not offset/gain compensated. That can be done with additional external circuitry and internal logic.

## Slide 3
Original Topology – 3-channel board DC analysis

## Slide 4
Original Topology – Results for subrange 0V-1V

## Slide 5: Sigma Delta Modulator – New Topology
+
-
Analog Input
D
Q
R
C
LVDS Receiver
Vref
clk
Board
PLD
Integrator
DAC
1-bit ADC
Digital
Output
R
Vref* | 1.650V
R | 4k7
C | 1nF
* Vref can be obtained by a resistor divider from VCCIO (3.3V)
Notes: - This is the block diagram associated

## Slide 6
New Topology - Comments
Advantages
  Good linearity across the whole range (0V to 3.3V)
  Better DC/AC performance than the original topology for the same input range
Disadvantages
  Requires the generation of a Vref on the board (the same Vref can/should be applied to all channels on the same chip)
  Requires the input signal source the ability to drive/draw current (typically < 1uA)
Comments
  Solution not yet characterised over process/temperature
  Differences in gain and offset (not only between 2 different devices, but also between 2 channels within the same device) – which means the output of the ADC is not offset/gain compensated. That can be done with additional external circuitry and internal logic.

## Slide 7
New Topology - 3-channel board DC analysis